SEAHU SH017 (PiToDin)
Hardware specification

PiToDIN (RaspbeeryPI to DIN)

DESCRIPTION
PLC computer based on raspberryPI on DIN case. Included monochrome display witch 5 buttons, rassperryPi B+ or v2 or v3 and base board witch 4x relay, RS235, RS485, 2x optical isolated output, 2x optical isolated input, buzzer, real time witch battery and 5V one wire interface. DIN case 6 module width.

HARDWARE SPECIFICATION:
4x Relays -	15A/	125V~
15A/	24V=
10A/	250V~
U 5 V
R 69 Ω
P 0,36 W
controlled by I2C 8bit PIO PCF8574 with I2C address 0x20
I2C One-wire master – DS 2482-100 more on http://datasheets.maximintegrated.com/en/ds/DS2482-100.pdf
with ESD protection and 5V output with polyfuse 0,5A. I2C address 0x18.
RS232 – only TX,RX
RS485 – share witch RS232, included jumper for terminator resistor.
Buzzer – connected to raspberryPi pin 12 (GPIO18)
Display – 1.4 inch Graphic 128x64 LCD Module Serial SPI ST7565 Black on White
5x Buttons – connected to I2C 8bit PIO PCF8574 with I2C address 0x24 Bit 6 is used as backlight display.
Real-time – connected to I2C RTC PCF8563 with I2C address 0x51 and battery backup.
2x optical isolated input – configure-able by jumpers on base board as isolated work in activate	range 3,3-12V, or usage internal voltage with activate by short. (use chip PC847).	Control by some chip as relays with bit 4,5.
2x optical isolated output – open collector max. 6V 50mA e.g. chip PC847 isolation voltage 5KV.	Control by some chip as relays with bit 6,7.
Power – 5V 2A by micro usb on raspberryPI or DC2,5mm connector.

Other specification by used raspberryPI computer https://www.raspberrypi.org .

MAIN BOARD:

1
2
3
4
5
6
7
8

12
13
14
15
17
16
9

11
10

DESCRIPTION:

1. C 2,5mm connector 5V 2A.

2. Serial connector (RS232).
   Pin 2 – RX
   Pin 3 – TX
   Pin 5 – GND
3. RS485
   1 – terminator resistor 120Ω jumper
   2 – B pin
   3 – A pin
   4 – GND

  4
  3
  2
  1
4. Antenna pin for options 433MHz module
5. 2x optical isolated output with open collector
   (use chip PC847)
   output1 – pin 1, 2
   output2 – pin 3, 4
   pin 1,3 – collector (max. +6V 50mA)
   pin 2,4 – emitter (0V)

   control by I2C 8bit register (chip PCF8574 or PCF8574A) with I2C address 0x20 or 0x38

  4
  1
  2
  3
  1, 3
  2, 4
Bit 0	Bit 1	Bit 2	Bit 3	Bit 4	Bit 5	Bit 6	Bit 7
raley1	raley2	raley3	raley4	input1	input2	output1	output2

1. 2x optical isolation input
   is configure-able by jumper explain bellow.
   Input1 – pin 3, 4
   Input2 – pin 1, 2
   pin 2, 4 – has negation logic 3,3-12V mens logic 0
   pin 1, 3 – by jumpers configuration 0V or 5V.

   control by some chip as output.

  2, 4

  +5V
  1, 3

  1
  2
  3
  4

  INPUT2
  INPUT1
2. Jumpers configure optical isolation input
  Jumpers
  INPUT1
  Jumpers
  INPUT2

  Pin 2, 4

  +5V
  Pin 1, 3
  3,3-12V
  0V

  Pin 2, 4

  +5V
  Pin 1, 3

  Activate by expernal power.
  Activate by short .
  (no need external power, but not galvanic isolation)
3. buzzer
   connected cross transistor to connected to raspberryPi pin 12 (GPIO18)
4. Jumper for short pin 1 and pin 5 in RJ12 one wire connector
   standard one wire connector use RJ12 connector with pin1 to 5V power slave devices. This mean then you can’t use telephone cable with RJ11 connector with no parasite power device. Some devices e.g from http://www.hw-group.com use power on pin 5. In these case simply short jumper. But careful some devices or systems may use on pin 5 RJ12 12V for power more consumes devices.

  Jumper
  Shor 1 and 5 pin on RJ12

  1W
  RJ12
5. RJ12 standard one wire connector
   control by I2C one wire master DS2482-100 with I2C address 0x18 and ESD protection.
   5V logical one wire data and 5V output is protected by 0,5 A poly-fuse.

  1
  2
  3
  4
  5
  6
  Looking into Female RJ12
  Connector
  PIN CONFIGURATION RJ12 CONNECTOR
  PIN	SIGNAL / NAME	DESCRIPTION
  1	VDD	5 V DC
  2	GND	Ground
  3	OW	1-Wire Data (only 5V level logic)
  4	GND	Ground
  5	N.C. / [VDD]	If jumper ON / then 5V DC / else No Connection
  6	N.C.	No Connection

6. Output 5V connector with poly-fuse 0,5A
   poly-fuse shared with 5V output in RJ12 connector.

  5V
  GND
7. 4x Relays
   relays is control by I2C 8bit register (chip PCF8574 or PCF8574A) with I2C address 0x20 or 0x38
  bit mapping:
Bit 0	Bit 1	Bit 2	Bit 3	Bit 4	Bit 5	Bit 6	Bit 7
relay1	relay2	relay3	relay4	input1	input2	output1	output2

relay characteristic:
15A/125V~
15A/24V=
10A/250V~

connection:

  OFF
  ON

  OFF
  ON

  OFF
  ON

  OFF
  ON
  relay1
  relay2
  relay3
  relay4
1. Battery for real time clock
   type: CR2032 3V
  Real time chip is PCF8563 on I2C bus with I2C address 0x51
2. Display and keyboard connector

   keyboard use I2C 5V bus controlled by I2C 8bit register (chip PCF8574 or PCF8574A) with I2C address 0x24 or 0x3C
   bit mapping
  1
  3
  5
  7
  9
  2
  4
  6
  8
  10
  pin1 – A0, PI pin18
  (GPIO24)
  pin3 - RST, PI pin22
  (GPIO25)
  pin5 – CS, PI pin24
  (GPIO08)
  pin7 - MOSI, PI pin 19
  (GPIO10)
  pin9 – SCLK, PI pin 23
  (GPIO11)
  pin2 – 3,3V
  pin4 – 5V

  pin6 – SLC, PI pin 5
  (GPIO03)
  pin8 – SDA,Pi pin 3
  (GPIO02)
  pin10 - GND
Bit 0	Bit 1	Bit 2	Bit 3	Bit 4	Bit 5	Bit 6	Bit 7
LEFT	RIGHT	UP	DOWN	OK	ESC	backlight display	Not use

Display 1.4 inch Graphic 128x64 LCD Module Serial SPI ST7565 Black on White
controlled by SPI 3,3V bus compatible with ST7565 LCD driver.
Example at http://m8051.blogspot.cz/2015/04/raspberry-pi-gpiospi-to-use-st7565-lcd.html
1. RaspberryPI 40pin connector.
2. Options module SYN115 / F115 433 MHz ASK Wireless Transmitter
  can by on:
  https://www.openimpulse.com/blog/products-page/product-category/syn115-f115-433-mhz-ask-wireless-transmitter-module/
  http://www.ebay.com/itm/433MHz-Transmitter-Receiver-Module-SYN115-SYN480R-ASK-Wireless-Module-/351350062982

  3,3V

  GND

  ANT
  RaspbeeryPI pin38 (GPIO20)
3. Options module 433MHz SYN480R ASK Wireless Receiver

  3,3V

  GND

  ANT
  RaspbeeryPI pin40 (GPIO21)
POWER SUPPLY:
Power 5V from 1-wire bus on pin 1 RJ12 connector or pin 5 if jumper on PBC is linked.
Max 2,3W.

DIMENSIONS:

46mm
68mm
90mm

94mm
33mm
49mm
65mm

6x modul (107 mm)

VIEWS:
3.5jack audio and TV out

front:

MicroUSB
otions power input

One Wire
4xrelay

5V output
Protected 0,5 A fuse

RS485 terminator
jumper
433MHz atene
back:

RS485

RS232

2x Optical
Isolated
output

POWER IN 5V
2,5A

2x Optical
Isolated
input

left:

4x USB 2.0
ETHERNET 100Mbs

inside:

RaspberryPI mini computer

### More informations:
- web raspberrypi project:	https://www.raspberrypi.org/
- web seahu:	http://www.seahu.cz

### Writer:
Ing. Ondřej Lyčka november 2016
Document version: 1.01